## Slide 1: Particle time of flight (PTOF): A diagnostic for simultaneous measurements of multiple nuclear bang times at the NIF
B. Reichelt1, N. Kabadi1, M. Gatu Johnson1, B. Lahmann1, J. Frenje1, C.K. Li1, F. Seguin1, G. Sutcliffe1, R. Petrasso1, H. Rinderknecht2, J.R. Rygg2, V. Glebov2, J. Knauer2, M. Rosenberg2, C. Stoeckl2, C. Sangster2, C. Forrest2,
H. Sio3, A. Moore3, E. Mariscal3, J. Kimbrough3, F. Barbosa3, H.S. Park3, S. Friedrich3, M.J. Eckart3, E. Hartouni3, A. MacPhee3, A. Zylstra3, K. Baker3, D. Schlossberg3, J. Williams3, S. Kerr3, R. Leeper4, J. Kilkenny5
1Massachussetts Institute of Technology, 2Laboratory for Laser Energetics, 3Lawrence Livermore National Laboratory, 4Los Alamos National Laboratory, 5General Atomics
LLNL-PRES-831505
PTOF can extract multiple nuclear bang time measurements from some shots
PTOF works with a principle similar to semiconductor radiation detectors– ionizing radiation incident upon a biased diamond frees electron hole pairs into the conduction band, where they are swept along by the bias and can be detected as an electric signal
Power supply applying bias voltage (-500V)
FTD10000
Ionizing Protons, Neutrons, or Photons
Freed electron-hole pair
6 GHz Tek Scope
The signal measured at the detector is a convolution of the burn history, time of flight variations from the energy spectrum, and detector + cable chain impulse response– by adjusting burn history parameters, a fit to experimental data is obtained
BT
Impulse Response
Measured and forward fit PTOF signal
PTOF can determine burn histories if they are although the width of the impulse response and time of flight broadening limits PTOF to only a bang time detector in most cases
PTOF can extract multiple nuclear bang time measurements from some shots, which can be used to constrain evolution and give insight into other physical processes
DD-n
X-rays