## Slide 1
DT+ 40Ar
40Ar(n,2n)39Ar(268 y), 40Ar(2n,g)42Ar(33 y)
Argon tracer release on N220124
R.N. Sahoo1, M. Paul1, C. Velsko2, A. Zylstra2, M. Tessler3, M. L. Avila4, C. Dickerson4, H. Jayatissa4, J. McLain4, R.C. Pardo4, K. E. Rehm4, R. Scott4, I. Toltsukhin4, R. Vondrasek4, T. Bailey5, L. Callahan5, A. Clark5, Y. Kashiv5, A. Nelson5, P. Collon5, U. Köster6, K. Zuber7, R. Schwengner8
1Hebrew U. of Jerusalem 2Lawrence Livermore National Laboratory 3Soreq Nuclear Research Center 4Argonne National Laboratory 5U. of Notre Dame
6Institut Laue-Langevin, Grenoble 7Technical University Dresden, Dresden 8Helmholtz-Zentrum Dresden-Rossendorf, Dresden
A noble-gas accelerator mass spectrometry platform at NIF for nuclear astrophysics: status report
Neutron-induced reactions in a DT high-density plasma at NIF
Thermodynamical conditions of plasma density, temperature, pressure and the neutron density in a laser-induced implosion of a DT-filled capsule at NIF are the closest laboratory analog to stellar conditions
We plan studying neutron-induced reactions:
40Ar(n,2n)39Ar(268 y), 40Ar(2n,g)42Ar(33 y)
(n,2n): monitor of fast-neutron flux (2n,g): monitor of extreme neutron density approaching stellar r process. The chemical inertness of the noble gas Ar allows for reliable collection of reaction products.
Ch J Cerjan et al. J. Phys. G: Nucl. Part. Phys. 45 (2018) 033003
Experimental method:
Noble-gas accelerator mass spectrometry
(NOGAMS) of Ar sample collected from NIF chamber after the shot.
NOGAMS at Argonne National Laboratory: production of highly-charged Ar8+ ions, acce-leration to 6 MeV/u, identification in a gas-filled magnetic spectrograph.
Calibration experiments were performed: 40Ar(n,2n)39Ar with 14 MeV neutrons 40Ar(2nth,g)42Ar with reactor thermal neutrons
RAGS Argon collection tests at NIF
Static vacuum test froze 15 cc STP argon onto 44 Kelvin collector foam. Recovered 98% from 1 gram charcoal in sample bottle.
Dynamic flow tests with 15 cc STP argon released into NIF Target Chamber on a shot. Two tests complete, chemical analysis needed for argon fraction.
  Test 1: gas from foam and end tank=148% based on pressure
  Test 2: gas from foam only=56% based on pressure
RGA signal
40
40
+ tracer